## Slide 1
H8-Z5-5 Board Rework
Fix 16550 RS-232 Handshaking Polarity
Only for boards Rev 1.0, 1.1, 1.2. & 1.3.

## Slide 2
Rework Instructions: (Only for Rev 1.0 and 1.1, 1.2, and 1.3)
1.0 Cut traces on side 2 of U11 (74LS14) on pins 8 and 9 as shown.

## Slide 3
1.1 Remove the following Components:
Q7 – 3904
R28 – 1K

## Slide 4
1.3 Solder wire between Q7 pin 1 (C) and pin 2 (B)
1.4 Solder wire between Pin 32 (U17) and resistor R30 pin 1.
Solder wire
CUT
CUT
Solder wire
Remove R28
Remove Q7

## Slide 5
Rework Instructions:
2.0 On side 2, solder a wire from U17 pin 32 to
R30 (1K) pin 1 as shown.

## Slide 6
Rework Instructions: Done!
3.0 Now the user should be able to run HDOS/CPM “/DTR and /RTS” handshaking without any issues.